## Slide 1
DCIT 207 • Computer Organization & Architecture
Session 2 Group Work
Performance Concepts
📋 Instructions • Each group tackles ALL tasks collaboratively • Present findings to the class (10 min max) • Every member must be able to explain any answer
Groups:
4–5 students
Time:
45 minutes
Tasks:
4 Challenges
Dr. Ben-Bright Benuwa • UEW • 2024/2025

## Slide 2
TASK 1
Microprocessor Speed & Techniques
Exploring how modern processors squeeze maximum performance using clever design tricks.

## Slide 3
TASK 1 • Microprocessor Speed Techniques
1
Name and explain any THREE techniques used by modern processors to increase instruction throughput. Give a real-world analogy for at least one of them.
2
Pipelining is described as similar to an assembly line. Draw a simple diagram (on paper) showing how 4 instructions can overlap in a 4-stage pipeline, then explain one major problem pipelining can face.
3
Speculative execution and branch prediction work together. Explain what happens in the processor when a branch prediction turns out to be WRONG. Why can this be a security concern? (Think about Spectre/Meltdown vulnerabilities — Google if needed.)
4
Superscalar processors issue more than one instruction per clock cycle. What hardware challenge must the processor solve to make this work safely?
💡 Tip: Re-read Slide 4 notes carefully — the full explanations are richer than the bullet points.

## Slide 4
TASK 2
Performance Balance & Memory Wall
When the processor is a race car but memory is a bicycle — what do engineers do?

## Slide 5
TASK 2 • Performance Balance & Memory Wall
1
The "memory wall" is a major performance bottleneck. Explain in your own words what the memory wall is and WHY it matters even when the processor is very fast.
2
List FOUR specific architectural strategies used to reduce the impact of slow memory access. For each strategy, write one sentence explaining how it helps.
3
Look at Figure 2.1 (I/O device data rates). Identify the device with the LOWEST data rate and the one with the HIGHEST. What is the ratio between them? What does this tell a system designer about I/O architecture?
4
Imagine a processor that runs at 4 GHz but main memory has a 100ns access latency. How many clock cycles does the processor waste waiting for one memory access? Show your calculation.
💡 Tip: For Q4: clock cycle time = 1 / clock frequency. Cycles wasted = latency / cycle time.

## Slide 6
TASK 3
Multicore, MIC & GPU Revolution
Why did chip designers stop racing clock speed and start stacking cores?

## Slide 7
TASK 3 • Multicore, MIC & GPU
1
Figure 2.2 shows that clock frequency leveled off around 2003 while transistor count kept rising. Using the concepts of Power density and RC delay from the slides, explain WHY clock speed could not keep increasing indefinitely.
2
A multicore chip places multiple simpler processors on one die instead of one complex processor. According to the slides, performance scales roughly with √(complexity increase) for a single processor but nearly doubles per extra core. Why is this a compelling argument for multicore design?
3
What is GPGPU (General-Purpose computing on GPUs)? Give TWO specific real-world applications where GPGPU is used today (you may search online for current examples).
4
Compare MIC (Many Integrated Core) and a traditional multicore CPU. In what type of workload would MIC have a clear advantage? In what workload would a standard dual-core CPU be sufficient?
💡 Tip: Think about the difference between parallelizable tasks (e.g., video rendering) and inherently sequential tasks (e.g., a single-threaded program).

## Slide 8
TASK 5
Benchmarking & Performance Measurement
Measuring performance fairly is harder than it sounds — the math matters.

## Slide 9
TASK 5 • Benchmarks, SPEC & Calculating Means
1
Using Table 2.2 data: Computer A runs Program 1 in 2.0s and Program 2 in 0.75s. Computer B runs them in 1.0s and 2.0s. Which computer is faster overall? Confirm using (a) total execution time, (b) Harmonic Mean of MFLOPS rates. Show ALL calculations. Why does AM of rates give a misleading answer here?
2
Explain the difference between SPEC SPECspeed and SPECrate metrics. Give a scenario where a business would care more about SPECrate than SPECspeed.
3
What is the Geometric Mean and why is it preferred over Arithmetic Mean when comparing NORMALIZED benchmark results? Use Table 2.3 to support your explanation — show what happens when you switch the normalization reference from Computer A to Computer B.
4
Design challenge: Your team must select a computer for a university's AI research lab (heavy floating-point matrix operations, running 24/7 with 50 concurrent users). Which SPEC CPU2017 metric(s) would you prioritize and why? List at least three benchmarks from Table 2.5(B) that are most relevant and justify each choice.
💡 Tip: Little's Law: L = λW. For benchmarking, always ask: 'Does this metric reflect my actual workload?'

## Slide 10
DELIVERABLES & GRADING RUBRIC
Written Report
All 4 tasks answered in full
Calculations shown step-by-step
Diagrams drawn neatly
Names & student IDs on cover
Max 6 pages (excluding diagrams)
Presentation
10 minutes max per group
Every member presents ≥ 1 task
Clear explanation of Amdahl's Law results
At least one diagram shown
Q&A readiness from any member
Grading Criteria
⚡ Pro tip: The best groups go beyond the slides — use the textbook notes, search online, and connect concepts to current technology!

## Slide 11
Good luck!
Think deeply, collaborate actively,
and let curiosity guide your answers.
"The best performance improvement is the transition from a nonworking state to a working state."
— John Ousterhout